## Slide 1
Instrument Configuration Application

## Slide 2
Problem Statement
Multiple instrument flavors, each with unique configuration settings (alarms, averaging times, etc.)
  Time intensive configuration
  Need long term historical data retrieval across multiple board interfaces (multiple parameter sets)
No way to configure TCP remotely

## Slide 3
High-level Design
Simple interface for configuring patient profiles remotely (hard-wired only) and securely across all instruments variants
Historical data retrieval (up to 4 days of non-contiguous parameter info)
Utilize existing API for instrument communication (TCP and Serial)
Event-driven MVC Architecture written in C++

## Slide 4
Design Considerations
Run-time polymorphism to support multiple comm protocols and profile types
Support read/write of profile data from/to instrument
  Config packets may not always arrive in deterministic fashion, use hash to determine “infotype”
Data parsing = bottleneck, use native array of structs for constant time insertion
  Handle continuous and one-shot events (list)
  Handle rollover cases

## Slide 5
Trend Request
Get Trend
Unzip Trend
Parse Master
Session File
Parse Master
Param File
Loop by
Trend Sample
Write to CSV
Trend Retrieval Process

## Slide 6
UI Considerations
Vanilla GUI (intended mainly for trained technicians)
Profile representation → tabbed list of combo boxes and editable fields
Event-driven adjustment of limits via “infotype” lookup
Save serializable workspaces to disk

## Slide 7
Nice To Have
Write to multiple instruments wirelessly
Support multi-threading for read/write/parse operations
Professional Reports Interface
Import old workspaces, identify configuration diff
Interpret supported profile info for instrument under configuration
Factory Method → Configure profiles and trend based on instrument flavor at run-time